Polaris Sportsman 3 Headlight Modification

Remove the top half of the headlight pod. Once the pod is removed locate the wire loom (On 1998 and earlier models, look for the smaller loom of the two. On 1999 and later models look for the loom that comes from the front of the hi-low switch.) Just inside the pod make a three-inch cut through the loom only, being careful not to cut the wires inside. Find a yellow and a green wire. (If you don’t find these wires you cut the wrong loom. Tape it up and cut into the other loom.)

Solder a short piece of wire to each end of the diode and slide on a piece of shrink tubing. Shrink the tubing on the solder joint covering all exposed wires up to the diode.

Using a splice terminal splice the end of the diode with the stripe to the yellow wire (hi-beam). Using another splice terminal connect the other end of the diode to the green wire (low-beam). Turn on the key and test the lights. If they do not work you have the diode in backwards. Resolder the diode in the reverse direction and shrink on new heat shrink tubing. Test the lights again.

If the lights are working correctly bind everything up with a good coating of electrical tape. This will keep all the connections secure from vibration and should provide adequate waterproofing. Be careful not to bend the wires on the diode too much or they may break. If they do, you need to get a new diode. Also, avoid using too much heat when soldering the diode, excessive heat can quickly ruin a diode.

Disclaimer: These instructions are provided for informational purposes only. The use of these instructions is performed at your own risk; no liability is implied or expressed. Incorrect installation could cause damage to you or your machine, including but not limited to electrical fires, short circuits or damage to any or all parts of your electrical system. If you do not understand electricity or the instructions provided above contact a professional for assistance or at the very least, the appropriate electrical schematic for your vehicle.